## Slide 1
Physics-Informed Neural Networks
for Additive Manufacturing
1D Stefan Problem — Phase Change & Solidification
• Goutam Kumar Biswas • Maddox Gonzalez
EML 5360 Project presentation
Based on:
Zhu, Liu & Yan (2021),
Computational Mechanics
67(2):619–635

## Slide 2: Background
Applications include
Aerospace
Medical Implants
Automotive Industry
Why this matters
Enables complex shapes & geometries
Supports rapid prototyping
Reduces material waste compared to subtractive manufacturing, and other manufacturing processes

## Slide 3: Research Gap and Questions
Research gap
Research Questions
▪ Most PINN literature handles smooth PDEs — phase change introduces a discontinuous source term that is poorly conditioned.
▪ Published PINN-AM studies rarely report implementation details or failure modes; reproducibility is limited.
▪ The trade-off between hard- and soft-BC enforcement is not systematically compared on the same problem.
▪ Q1. Can a PINN reproduce a 1D Stefan AM solidification problem to FEM-level accuracy?
▪ Q2. Does hard-BC enforcement outperform soft-BC penalties in convergence and final loss?

## Slide 4: Project Objective
Reproduced the Zhu–Liu–Yan (2021) PINN framework on a 1D Stefan solidification problem, compare hard- vs soft-boundary enforcement, and benchmark the trained PINN against FEM across four mesh resolutions
Implementation of PINN using PyTorch.
FEM reference solver at four resolutions
Quantitative comparison: training loss, temperature snapshots, interface tracking, L₂ error.

## Slide 5: Related Work — PINNs and AM Thermal Modelling
Study
Contribution
Domain / PDE
Reported limitation
Raissi et al. (2019)
Introduced PINNs
Burgers, Schrödinger
Smooth PDEs only
Zhu, Liu, Yan (2021)
PINN for AM melt pool
1D Stefan, 2D steady
No BC-type comparison
Wang et al. (2022)
NTK analysis of PINNs
Convection-diffusion
Loss-weight sensitivity
Liao et al. (2023)
Adaptive sampling
Transient heat
Case-specific tuning
McClenny
&
Braga-
Neto
Self-adaptive weights
Benchmark PDEs
No phase-change test
Gap addressed by this project: none of the above directly compare hard- vs. soft-boundary enforcement on
the same phase-change problem with a matched FEM reference across multiple resolutions. This study fills
that gap and documents the practical training failure modes other papers omit.

## Slide 6
Domain
A bi-material rod representing an AM deposit:
change)
liquid phase change)
Boundary conditions
(Dirichlet)
Objective: Predict T(x,t) and interface s(t) betterthan FEM, without labelled interior data.
Problem Setup (1D Stefan)
Property
Al (liq)
Al (sol)
Graphite
ρ [kg/m3]
2555
2555
2200
κ [W/m K]
91
211
100
cp [J/kg K]
1190
1190
1700
L [kJ/kg]
398
398
—

## Slide 7: Governing Equation
Term-by-term:
PDE residual (PINN physics loss):
Liquid fraction (mushy zone)
Enthalpy-based heat equation form Zhu et al.

## Slide 8
FEM Reference — Mesh Refinement Study
Setup
1D FEM solver on Ω= [−0.4, 0.4] m,
t ∈ [5, 10]s
Enthalpy form with apparent heat-capacity for
latent heat
Dirichlet BCs: Tlb =298.15 K, Tub =973.15 K
Matched coarsening: Nt = Nx
Four resolutions
Nx ∈ { 50, 100, 150, 200}
Reference (“truth”): fine FEM on 401×201 grid
Nx
∆x [m]
Nt
∆t [s]
50
1.6×10−2
50
0.20
100
8.0×10−3
100
0.10
150
5.3×10−3
150
0.067
200
4.0×10−3
200
0.050
401*
2.0×10−3
201
0.050
Used for: L2-error benchmark vs. PINN and
interface tracking s(t)

## Slide 9
Init: Xavier uniform: used to initialize the
weights of neural network
Input normalization
:
Hidden Layer 1 (200)
... (4 layers total)
Hidden Layer 4 (200)
Methodology PINN Architecture
Activation (Paper) :
Activation (Our) :

## Slide 10
Loss
:
IC + PDE only (2 objectives)
Advantage:
exact BC, fewer competing terms
Loss
:
IC + BC penalties + PDE (4 objectives)
Challenge:
balance
4
objectives,
risk
of
saddle-
point collapse
Shared hyperparameters:
PINN Hard BC vs. Soft BC Enforcement

## Slide 11
Stage 1 — Pre-training
(IC fit only)
Initializes weights in a physically meaningful
state
Stage 2 — Main training
(IC + PDE + BC)
Analogy
:
Adam = hiker finding the valley;
L-BFGS = GPS robot locating the exact minimum.
PINN Training Procedure
Set
Symbol
Count
Initial condition
N0
300
Boundary (Soft only)
Nb
100
Collocation (LHS)
Nf
40,000
LHS = Latin Hypercube Sampling; ensures uniform
coverage without regular-grid repetition.

## Slide 12: Training Data & PINN Prediction Field
(a) Training data layout in (t, x): collocation (black), IC (red), BC
(green)
(b) Predicted temperature field T(x, t) from the Hard-BC PINN
The PINN is mesh-free: once trained, T(x, t) is evaluated at any (x, t) in microseconds.

## Slide 13: Geometry and Prediction
a)
b)
c)
d)
Our PINN model prediction
Zhu et al PINN model prediction
Fig: Predicted temperature field T(x, t) from the Hard-BC PINN

## Slide 14: Training Loss comparison
a)
b)
c)
d)
Our PINN model Training loss
Zhu et al PINN Training loss

## Slide 15: Temperature prediction comparison
a)
b)
c)
d)
Our PINN model temperature prediction
Zhu et al PINN model temperature prediction
Both Hard- and Soft-BC PINN predictions track the FEM reference across the domain, including the mushy zone near
x ≈ 0–0.1 m.

## Slide 16: Solid--Liquid Interface Tracking- PINN comparison
Our PINN model interface prediction
Zhu et al PINN model interface prediction
Fig: PINN interface at N = 50, 100, 150, 200 collocation points

## Slide 17: FEM mesh study comparison
Our FEM temperature prediction
Zhu et al FEM temperature prediction
Fig: FEM interface s(t) at Nx = 50, 100, 150, 200 (Nt = Nx)

## Slide 18: Results — L2 Resolution Study
Resolution Nx
FEM L2 (Our)
FEM L2 (paper)
PINN L2 (Hard)
PINN L2 (Soft)
∆ FEM vs. PINN
50
3.6×10−2
3.7×10−2
1.1×10−3
2.4×10−3
FEM ≫ PINN
100
9.1×10−3
9.3×10−3
1.0×10−3
2.2×10−3
FEM > PINN
150
4.1×10−3
4.2×10−3
1.0×10−3
2.1×10−3
FEM > PINN
200
2.3×10−3
2.4×10−3
0.9×10−3
2.0×10−3
FEM ≈ PINN
Key observations
FEM error scales as Nx— requires Nx ≥ 200 to match the PINN accuracy.
PINN error is set at training time — resolution-independent, no post-hoc tuning.
At Nx ≤ 150: single trained PINN outperforms FEM with zero re-computation cost.

## Slide 19: L2 norm prediction error
Our L2 error
Zhu et al L2 error
Relative L2 error vs. spatial resolution Nx | Reference: fine FEM on 401×201 grid

## Slide 20: Conclusion
Temperature profiles: PINN ≈ FEM
reference
Interface tracking: matches analytic
s∗(t)
L2 study: FEM > PINN at Nx ≤ 150
Matches paper Fig. 6
Mesh-free: evaluate at any (x, t)
Resolution-independent: one net ≡all Nx
Physics-constrained: PDE embedded
Data-efficient: IC from FEM at t0 only
Summary: PINN trained on the 1D Stefan problem achieves accuracy comparable to a fine FEM solution, However
while remaining mesh-free

## Slide 21: Weaknesses & Future Work
Future work
Uncertainty quantification — Bayesian
PINN or ensembles.
Real AM integration — laser boundary
source, 3D multi-layer deposits.
2D extension — PINN advantage grows as
FEM cost scales ∼ N2.
Potential weaknesses
. IC relies on a FEM reference at t_0 — not fully data-free
. Only 1 dimension is taken into account

## Slide 22: References
[1] Q. Zhu, Z. Liu, J. Yan, "Machine learning for metal additive manufacturing: predicting temperature and melt pool fluid dynamics using physics-informed neural networks," Computational Mechanics 67(2): 619-635, 2021. DOI: https://doi.org/10.1007/s00466-020-01952-9
[2] M. Raissi, P. Perdikaris, G. E. Karniadakis, "Physics-informed neural networks: a deep learning framework for solving forward and inverse problems involving nonlinear partial differential equations," Journal of Computational Physics 378: 686-707, 2019. DOI: https://doi.org/10.1016/j.jcp.2018.10.045
[3] S. Wang, Y. Teng, P. Perdikaris, "Understanding and mitigating gradient flow pathologies in physics-informed neural networks," SIAM Journal on Scientific Computing 43(5): A3055-A3081, 2021. DOI: https://doi.org/10.1137/20M1318043
[4] S. Liao, T. Xue, J. Jeong, S. Webster, K. Ehmann, J. Cao, "Hybrid thermal modeling of additive manufacturing processes using physics-informed neural networks for temperature prediction and parameter identification," Computational Mechanics 72(3): 499-512, 2023. DOI: https://doi.org/10.1007/s00466-022-02257-9
[5] L. D. McClenny, U. M. Braga-Neto, "Self-Adaptive Physics-Informed Neural Networks using a Soft Attention Mechanism," arXiv, 2020. DOI: https://doi.org/10.48550/arXiv.2009.04544
Thank you — Questions?